1. Create Oem Image

Tracking antenna Ip configuration
trackingAntennaIPArr[0]="192.168.10.11"
trackingAntennaIPArr[1]="192.168.10.12"
trackingAntennaIPArr[2]="192.168.10.13"

Laptop ip configuration
laptopIPArr[0]="192.168.10.21"
laptopIPArr[1]="192.168.10.22"
laptopIPArr[2]="192.168.10.23"

Flash on remote controller

2:Router Configuration :

Open Browser :
type : 192.168.10.1 or 192.168.1.1

i) Change name of the router
Basic > Wireless > Set name : RM/MR10_X8/23/19
click on Save.

ii) Do all the ips static using router.

Advance Setting > Network > LAN Settings
click on Add > Scan > modify the ip
below address will be configured
Router ip: 192.168.10.1
Coral Tracking antenna ip: 192.168.10.11
Laptop Ip: 192.168.10.21
Remote Controller (Herelink) : 192.168.10.31

3. Coral Configuration

Coral is creating Hotspot so It was not connecting with Wifi. So we have to comment in hotspot configuration.
Open coral using ssh.
Suppose coral ip is : 192.168.10.110

Linux terminal : ssh@192.168.10.110
or
 open connect with HDMI and keyboard and mouse
and type
$ifconfig

//commect all the code written inside the file
coral home $ sudo nano /etc/hostapd/hostapd.conf
coral home $ sudo nano /etc/dnsmasq.conf
coral home $ sudo nano /etc/network/interfaces

coral home$ reboot

coral home$ nmtui
Activate connection

Wireless connection > select : >
SSID : RM/MR10_X8/23/19
Security : WPA & WPA2 Personal

[X] Automatically Connect
[X] Available to all users
click on OK

4. MFO configuration for laptop data and video
Connect laptop with RM/MR10_X8/23/19
Settings > Commlinks > Add >
Drop Down: UDP
Listening Port : 23001

Connect the com port and then connect

Issue : Slow data transfer on e-GCS(laptop AppImage)
Reason : During the communication the Component id are the same laptop and herelink RC. So we have to change the id.
Settings > MAVLink > 254